## Slide 1: Quinzhee Construction
Reminders and Steps

## Slide 2: Reminders
NOTHING LEFT IN THE ­­­SNOW
STAND OBJECTS RIGHT SIDE UP IN THE SNOW WHEN NOT IN USE
MANAGE YOUR SHRAPNEL
STAY ACTIVE AND CARE FOR YOURSELF TO REMAIN WARM, DRY AND COMFORTABLE
NEVER BUILD A FIRE OR COOK INSIDE A QUINZHEE AS THE RISK OF CARBON MONOXIDE POISONING IS HIGH

## Slide 3: Step 1
Find a level area with at least 30 cm of snow.

## Slide 4: Step 2
Mark out an egg shape a couple of feet longer and wider than the sleeping arrangement.

## Slide 5: Step 3
Compact the snow within the egg shape by stepping on it, spiralling outward from the centre

## Slide 6: Step 4
Heap and pack a layer of snow onto the egg-shaped outline and compact it in the same spiral formation from step 3

## Slide 7: Step 5
Continue step 4 until you have a mound of snow in the shape of an upside down bowl (convex, not concave or conical) which is taller than you. Use shovels and body weight to help compact the snow from the outside.

## Slide 8: Step 6
Collect a few dozen finger thickness sticks that are 30 cm long. Insert them half way into the walls and roof so that your snow mound resembles a porcupine.

## Slide 9: Step 7
Allow the mound to sinter for at least 3 – 5 hours, overnight is best, depending on the crystal type and temperature.

## Slide 10: Step 8
Assess wind direction and work at 90 degrees to it for platform/ door construction.

## Slide 11: Step 9
Begin by making a trench just above knee level, carving out the inside of the quinzhee, ceiling first then walls, but not surpassing the porcupine sticks (i.e. 15 cm wall thickness). The sleeping platform should be made flat at about knee height. Work with a partner to move snow away from the trench.

## Slide 12: Step 10
Construct the door across from the trench from the bottom of the quinzhee upward to the sleeping platform. Carve a step out of the snow if wanted/ needed.

## Slide 13: Step 11
Snow from the trench can be moved to reinforce the door area and provide additional shelter from the wind.

## Slide 14: Step 12
Block the trench with hard pieces of snow and throw shovels of soft snow at it to close any holes.

## Slide 15: Step 13
Carefully make a fist sized air hole through the ceiling.

## Slide 16: Step 14
Lay your tarp out on the sleeping platform and your sleeping mats/ bags on top of it.

## Slide 17: Step 15
Sleep with the doorway blocked by a bag and with a shovel inside your quinzhee.